## Slide 1: Efficient mitigation of RFI at radio astronomy observatories
Thomas Krenz
Product Manager
Spectrum Monitoring Systems

## Slide 2: The theory
Various frequency bands are (exclusively) assigned to radio astronomy
Example: German Frequency Allocation Plan
Range | # Bands | Total bandwidth
HF | 2 | 170 kHz
V/UHF | 14 | 106 MHz
SHF | 12 | 1,1 GHz
EHF | 52 | 175 GHz
Radio astronomy
1400 MHz
1427 MHz

## Slide 3: The larger picture
You are here
Notes: So does everybody else …

## Slide 4: The real life
National regulators have to ensure interference free environment
In many countries regulators react slower than expected
Consequently, many companies and organizations defend their spectrum themselves
Typically, they use ITU-compliant equipment

## Slide 5: The customer specific solution
Benefits of using the same equipment as local regulator
  Credibility
  Hassle-free data exchange
  Potential sharing of hardware
  Security

## Slide 6: Lessons learned from 120 countries
Points to ponder when planning RFI measurements
  Why?
    Check current situation before important mission
    Understand long term situation
    Locate / identify interferer
    Collect data for complaint to local regulator
  Short term or long term measurements?
    Low duty cycle signals / time variant interferers
    Larger amount of data -> requirement for automated processes and sophisticated data reduction
  Where to put the equipment?

## Slide 7: Lessons learned from 120 countries
Points to ponder when planning RFI measurements
  Omnidirectional or directional antenna?
    Omni is faster -> better time resolution -> detection of burst
    Directional provides location information and has higher sensitivity
  Measurements for both polarization necessary?
  Average or MaxHold?
  Calibrate !!!

## Slide 8: The customer specific solution
Special requirements for radio astronomy observatories
  Efficient, easy operation
  Fully automatic procedures
  Frequency coverage according to astronomy bands
  Technical specifications matching the specific demands, e.g. sensitivity, linearity, dynamic range, …

## Slide 9: The customer specific solution
Selected equipment
Hardware
  Compact, autonomous monitoring systems
  Location finding systems
  Handheld equipment
Software
  Dedicated spectrum monitoring control software
  Fully automatic operation
  Real-time interference detection, identification and localization
  Provide necessary information so that other systems can follow-up

## Slide 10: The customer specific solution UMS300
Compact outdoor system
ITU – compliant
Monitoring, DF, TDOA
Minimum infrastructure requirements

## Slide 11: The customer specific solution UMS300
1 = Peltier element
2 = System computer
3 = Power control board
4 = Connection panel
5 = 3/4G modem
6 = Antenna selection switch
7 = Receiver
8 = Router
9 = SSD drive

## Slide 12: The customer specific solution UMS300
Monitoring
  Frequency range 9 kHz – 26,5 GHz
  Optional up to 256 GHz
  Multichannel digital down conversion (DDC) within real-time bandwidth
  I/Q recording

## Slide 13: The customer specific solution UMS300
Direction finding
  Wideband DF mode
  DF antennas with active / passive switching
  DF antennas for horizontal / vertical polarization

## Slide 14: The customer specific solution Mobile monitoring systems

## Slide 15: The customer specific solution PR100
Handheld monitoring receiver

## Slide 16: The customer specific solution
Monitoring receiver vs. spectrum analyzer
Different device types developed for different applications
Monitoring receiver – real world Spectrum analyzer – laboratory environment

## Slide 17: The customer specific solution
Monitoring receiver vs. spectrum analyzer
Monitoring receiver
  Unknown signal scenario (frequency, level, modulation, timing, …)
  Signal fed via antenna
  Signal can not be influenced by operator
  Measurements can (often) not be repeated

## Slide 18: The customer specific solution
Monitoring receiver vs. spectrum analyzer
Spectrum analyzer
  Known signal scenario
  Signal fed via cable
  Signal can easily be influenced by operator
  Measurements can be repeated

## Slide 19: The customer specific solution ARGUS control software
Real-time comparison of live results with reference data

## Slide 20: The customer specific solution ARGUS control software
Real-time comparison of live results with reference data

## Slide 21: The customer specific solution ARGUS control software
Identification of interferer

## Slide 22: The customer specific solution ARGUS control software
Identification of interferer

## Slide 23: The customer specific solution ARGUS control software
Sophisticated antenna control

## Slide 24: The customer specific solution ARGUS control software
Automatic multi-tasking according to schedule

## Slide 25: The customer specific solution ARGUS control software
Continuous monitoring with smart data reduction

## Slide 26: Summary
Radio frequency interference exists
Rohde & Schwarz has dedicated, proven tools to mitigate RFI
Don’t miss the Nobel Prize because of RFI